USER MANUAL

TIRE CHANGER

INDEX

Preface and Warning…………………………………………………………2

- General Description…………………………………………………………3

- Mounting tool Usage…………………………………………………………4

- Installation……………………………………………………………………5

- Operation……………………………………………………………………6

- Maintenance……………………………………………………………….9

- Transportation………………………………………………………………10

- Accessory……………………………………………………………………11

- Circuit Diagram..……………………………………………………12

Note: If machine comes with quick tire inflating system and helper, please read the user manual for quick tire inflating system and helper.

Preface

Thanks for choosing this tire changer. This tire changer has the following remarkable features:

- It works with pneumatic locked device on better reliability, the vertical arm is back tilting design. Convenient dismount, time saving and better repeatability can guarantee good operation.

- The Max. rim diameter is 24” and also be suitable for low-profile tire.

- With the merits of reasonable design, good materials, reliability, convenient operation and long working time, it is popular in the market. Details in the manual.

Warning

- Please read the manual earnestly; Pay attention to operation rules.

- Limited operation range: The manual and technical assist from manufacturer.

- Don’t operate for other purpose. Manufacturer will not be responsible for the losses caused by refitting without permission.

- Cut off electricity supply if there is something wrong during operation, and then deal with troubles.

- Wear protecting clothes during operation.

1. General Description

1.1 Technical Data

| Air pressure | 8-10bar |
| --- | --- |
| Motor | 220V/50Hz |
| Operation temperature | 0℃—45℃ |
| RPM of turntable | 6rpm |
| Max. depth | 1620mm (including tilting room) |
| Max. width | 1220mm |
| Max. height | 1920mm |
| Net. weight | 215kg |
| Max. tire width | 330mm |
| Max. tire diameter | 1010mm |
| Rim clamping diameter (outer) | 13″—24″ |
| Rim clamping diameter (inner) | 11″—22″ |

1.2 Parts

- Turntable control pedal

- Bead breaker control pedal

- Clamp control pedal

- Tilting back post control pedal

- Clamps

- Turntable

- Oil-water separator with shelf

- Mounting tool

- Vertical hexangular rod

- Handle

- Horizontal arm

- Tilting back post

- Lubricant cup

- Bead breaker shelf

- Bead breaker

- Rubber protector

- Lever

Fig. 1

1.3 Operation System (parts no. refer to fig 1)

1.3.1 Turn on the pneumatic switch on the handle (10), move the vertical hexangular rod (9) up and down, move the horizontal arm (11) from front to back, all steps get ready for mounting/dismounting tire.

1.3.2 After adjusting mounting tool（8）, push pneumatic switch on the handle (10), lock mounting tool (8) and horizontal arm (11) tightly, mounting tool (8) is ready for operating.

1.3.3 Mounting tool (8) mounts or dismounts tire from rim with the help of lever (17).

1.4 Turntable with centering automatically (parts no. refer to fig 1)

1.4.1 Turntable (6) is used for fixing and rotating rim, and composed by two cylinders with centering automatically.

1.4.2 Fix rim by inside or outside clamps (5).

1.4.3 Rotating turntable (6), rotate clockwise or counter-clockwise with rim by electrical machine and gear box.

1.5 Foot pedal control system (parts no. refer to fig 1)

1.5.1 Step on turntable control pedal (1) and rotate turntable clockwise, push-up the pedal and rotate turntable counter-clockwise.

1.5.2 Step on bead breaker control pedal (2) and bead breaker operates from outside to inside, dismount tire from the rim.

1.5.3 Clamp control pedal (3) is used for open or close clamps.

1.5.4 Step on tilting back post control pedal (4) and leave the vertical post (12) tilt back, step on the pedal (4) again, push-up pedal and leave vertical post (12) upright.

1.6 Bead breaker (parts no. refer to fig 1)

1.6.1 Move bead breaker shelf (14) drivened by cylinder repeatedly.

1.6.2 Bead breaker (15) is used for pressing tire.

1.6.3 Rubber protector is used for tire protecting and rim anti-gliding during dismounting.

2. Mounting tool Usage

2.1 Operation (parts no. refer to fig 1)

2.1.1 After loosening tire, open or close clamp to fix the tire on the turntable (6).

2.1.2 Step on pedal (4), leave vertical post (12) upright.

2.1.3 Control horizontal arm (11) by handle (10), press vertical hexangular rod (9) and adjust mounting tool (8) to the best position for operating (see fig. 9). Push pneumatic switch on the handle (10) (see fig. 10), lock vertical hexangular rod (9) and horizontal arm (11) tightly.

2.1.4 Mount or dismount tire follow normal steps.

3. Installation

“ ! ”warning: 1. Leave equipment 500mm space from the wall for convenient operation.

2. Don’t put the equipment in the open-air or wet place.

3.1 Put machine on the concrete ground and fix it by M10 expansion bolt.

3.2 Link pneumatic supply with oil-water separator. (see fig 3)

Fig. 3

3.3 Electric System Installation

1) Electric system must be installed and operated by professional staff. .

2) Make sure to link with ground for safety purpose.

3.4 Troubles and repairs during installation

| Trouble | Reason | Repair |
| --- | --- | --- |
| Turntable doesn’t rotate. | 1.Plug is not linked. 2.Electric supply is not right. | Check and correct plug |
| Rotating speed is too low | 1.Power supply and voltage are not right. 2.Transmission belt is relaxed. | 1.Check power supply and voltage, they must accord with signs set by machine. 2.Tighten transmission belt. |
| Turntable can’t lock rim | 1.Pneumatic device and machine are not linked. 2.Pressure of pneumatic system is not enough. | 1.Link pneumatic supply 2.Correct pressure |

- Operation

“ ! ” warning: Tire changer installation and operation only by trained professional staff!

4.1.1 Dismount operation (see fig.4)

1) Air exhausting

2) Take out air inflating entrance.

3) Take out counterweights

Fig.4

4.1.2 Separate tire (see fig.5)

1) Lubricate rim and edge.

2) Put the tire near the rubber protector, adjust shelf to 1cm from outside tire, and adjust accurately

by rod.

3) Step on pedal and separate.

4) Rotate wheel left and right by hand, to do so repeatedly until separate completely..

5) Change the other side and repeat above actions.

Fig 5                                  Fig 6

4.1.3 Clamp wheel tightly

1) Release pneumatic lock of tire changer before clamping wheel and move mounting tool to the top, and push horizontal arm to the back, then re-lock it, step on tilting back post control pedal to slant vertical post to back.

2)Clamp 13”-24”rim from inside to outside.(see fig 6)

●Put the wheel (rim) on the turntable

●Step on clamp control pedal and the wheel is clamped tightly.

●Step on clamp control pedal to”stop”, and loosen the pedal, as well as the wheel.

3)Clamp 11”-22”rim from outside (fig 7)                            Fig 7

●Step on clamp control pedal(3) and loosen, move clamps to outside.

●Put on rim or wheel.

●Step on clamp control pedal(3) and loosen, the wheel is clamped tightly.

●Always clamp ALU rim from outside to protect preface.

4.2 Mounting tool setting

1) Push horizontal arm back thoroughly and leave dismounting head to the top before mounting and dismounting tire. If the wheels have the same dimension, you need not to change the position. (see fig 8)

2) Move the mounting tool to touch the rim both on top and on side, then fix the mounting tool.The mounting tool will automatically go 3mm up and 3mm back.Check the distance between the mounting tool and the rim, if not enough, then adjust the gap by fix the mounting tool again as shown on fig 8.

3) When the rim is more than 23” and less than 8”, re-adjust

mounting tool and rim.                                          Fig 8

4) Loosen screw (1) of tire changer, adjust screw(2) to make it suitable, leave 3-5mm from (3) to rim edge.(see fig 9)

5) Re-rotating screw (1) after adjusting.(see fig 9)

6) The way to fix mounting tool (see fig10):

Push in the button on the handle, that’s mean mounting tool is locked at fixed position. Push out the button after mounting and dismounting that’s mean opening the lock and the mounting tool can move vertically and horizontally (see fig10)

“ ! ” warning: 1) Mounting tool rolling ball and rim edge are non-contacted. 2) Use nylon protectors when you mount or dismount alloy rim.3) The angle of mounting tool has been adjusted according to 14”normal rim before leaving manufacturer, please re-positioning mounting tool if the rim is too big or small.

Fig 9                                  Fig 10

4.3 Dismounting tire

1) Lock rim to the turntable.

2) Lubricate rim and edge before dismounting tire.

3) Step on tilting back post pedal (4), make horizontal arm into working position.

4) Rotate and adjust wheel to let the tire inflating valve in front (10cm) of mounting tool.

5) Set operation according to 5.2

6) Prize the tire by lever.

7) Step on turntable control pedal (1), rotate the turntable clockwise, which make rim edge into the flute until finishing dismounting. (see fig11)

8) Take out inside tire if there is. Repeat above steps and dismount the other rim edge. (see fig12)

9) Step on pedal (4) after dismounting, tilt horizontal arm to the back.

Fig 11                                   Fig 12

4.4 Tire installation

“ ! ” warning: check dimension of tire and rim before installation.

  - Lubricate rim and edge.

  - Clamp rim tightly, 180 degree between tire inflating valve and mounting tool.

  - Step on tilting back post control pedal (4), horizontal arm go into working position.

  - Set operation model according to 4.2. Put rim edge on the top of mounting tool, step on turntable control pedal (1), rotate turntable clockwise, and make the rim edge into rim groove.

  - Put down the bead pressing wheel if new,            Fig 13

low-profile and stiff tire, at the same time near the bead pressing wheel device, press bead

pressing wheel manually and rotate turntable clockwise. Mounting tire finishes. (see fig 13)

  - When you mount the upper tire, loosen the bolt of the bead pressing roller, rotate the bead pressing roller in front of the dismounting head, and fasten it with bolt.(fig 14)

  - When the upper tire is rotated to 10-20cm away from the dismounting head, put the bead pressing device on the rim edge, which is helpful to mount and dismount the low-profile stiff tires.(fig 15)

  - After the installment, dismount the bead pressing device, and lift up the bead pressing roller, then rotate it to the rim center.

“ ! ” warning : 1) If the rim dimension is same, only step on tilting back post control pedal(4).

2) Watch during clamping rim to avoid being hurt.

(Fig 14)                                       (Fig 15)

4.5 Inflating

The machine is equipped with quick tire inflating system, please read the user manual for quick tire inflating system.

5. Maintenance:

“ ! ” warning:1. Clean and maintenance should be done by professional staff according to following instructions. 2. Cut off electricity and pneumatic supply before repair.

- Make sure that there is sufficient lubricant in oil-water separator and adjust oil amount. (see fig 16)

- Add SAE 10W ISO 32 oil regularly.

- Driven off the waste water from oil-water  separator.

- Clean all parts on the turntable.(see fig 17)

Fig 16                                      Fig 17

- Check and tighten all bolts of joint parts regularly.

- Keep hexangular vertical spindle clean and dry

(oil for cleaning)

- The combination of friction between surface

should be lubricated by Lithium lipid oil.

- Check and adjust the tension of transmission belt.

(see fig 18)

- Keep machine and operation zone clean, avoid

dusted parts.

Fig 18

6.Transportation

“ ! ” warning: Pay attention to equipment barycenter to avoid slanting over.

- Transported with virgin packing.

- Put away refer to packing

- Transit by fork-lifter (see fig 19)

- Keep vertical arm and horizontal arm stay at

the appropriate position.

- Transmission speed is appropriate.

Fig 19

- Accessory

Lubricant cup and brush               Clamp protectors              Nylon washer

Lever                        Lever protectors          Bead breaker protectors

plastic clip                           arm roll

(for low profile tire)                  (for low-profile tire)

- Circuit diagram

“ ! ” warning:

1.  All electricity installation should be done by professional electricians.

2.  If the voltage is 220V, please guarantee voltage stability, so as to avoid damaging capacitance.

9 Separate parts picture and list

| No. | Sequ.No. | Name | Qua. | Spec. | No. | Sequ.No | Name | Qua. | Spec. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0101 | Vertical arm | 1 |  | 33 | 0133 | Limit washer | 1 |  |
| 2 | 0102 | Hexangular shaft of vertical arm | 1 |  | 34 | 0134 | Pipe safety | 1 |  |
| 3 | 0103 | Valve for locking | 2 |  | 35 | 0135 | Block of horizontal arm safety | 2 |  |
| 4 | 0104 | Y-ring | 2 | 60 | 36 | 0136 | Round bolt | 2 | M6X25 |
| 5 | 0105 | Valve cover for locking | 2 |  | 37 | 0137 | Rolled roller | 1 |  |
| 6 | 0106 | Horizontal locking-board | 1 |  | 38 | 0138 | shaft | 1 |  |
| 7 | 0107 | Vertical locking-board | 1 |  | 39 | 0139 | Hexagon nut | 2 | M8 |
| 8 | 0108 | Bilateral bolt | 2 | M12X30 | 40 | 0140 | Front thread washer | 1 |  |
| 9 | 0109 | Shelf for cover of horizontal arm | 1 |  | 41 | 0141 | Six-angular bolt | 1 | M8 |
| 10 | 0110 | Round bolt | 1 | M8×10 | 42 | 0142 | pad | 2 |  |
| 11 | 0111 | Hexangular spring | 1 |  | 43 | 0143 | Flat washer ring | 2 | D8 |
| 12 | 0112 | Hexangular shaft cap | 1 |  | 44 | 0144 | Six-angular nut | 2 | M8 |
| 13 | 0113 | Round bolt | 1 | M10×30 | 45 | 0145 | Six-angular bolt | 2 | M12X30 |
| 14 | 0114 | Horizontal arm safety | 1 |  | 46 | 0146 | Flat ring | 1 | D12 |
| 15 | 0115 | Switch | 1 |  | 47 | 0147 | Ring for shaft | 1 | D12 |
| 16 | 0116 | Round bolt | 4 | M5X10 | 48 | 0148 | Six angles locking bolt | 2 | M12 |
| 17 | 0117 | Round bolt | 1 | M8X16 | 49 | 0149 | Six-angular bolt | 1 | M10X16 |
| 18 | 0118 | Ring for mounting head | 1 |  | 50 | 0150 | Six-angular nut | 2 | M12 |
| 19 | 0119 | Mounting head | 1 |  | 51 | 0151 | Six angles locking bolt | 2 | M8x25 |
| 20 | 0120 | Bead pressing roller assembly | 1 |  | 52 | 0152 | Taper roller | 1 |  |
| 21 | 0121 | Flat ring | 1 | D10 | 53 | 0153 | Top thread | 1 | M6x24 |
| 22 | 0122 | Round bolt | 2 | M10X25 | 54 | 0154 | Limit rubber washer | 1 |  |
| 23 | 0123 | shaft | 1 |  | 55 | 0155 | Nut | 2 | M10 |
| 24 | 0124 | Large pad of vertical arm | 2 | D10 | 56 | 0156 | PV pipe | 1 | Φ6 |
| 25 | 0125 | Round bolt | 4 | M6×35 | 57 | 0157 | PV pipe | 1 | Φ6 |
| 26 | 0126 | Spring of hexangular locking board | 2 |  | 58 | 0158 | Tee joint | 1 | D6 |
| 27 | 0127 | Stud bolt | 2 | M8X60 | 59 | 0159 | PV pipe | 1 | Φ6 |
| 28 | 0128 | Bolt for tightening | 2 | M10X10 | 60 | 0160 | Inserting tee joint | 2 | D6 |
| 61 | 0161 | Spacer | 3 |  | 65 | 0165 | Round nut | 2 | M6 |
| 62 | 0162 | O-ring | 3 | Φ8x2.65 | 66 | 0166 | Right angle terminal pipe joint | 1 | D6 |
| 63 | 0163 | Pressing cover | 1 |  | 67 | 0167 | Protect slice for tire | 1 |  |
| 64 | 0164 | Valve rod | 1 |  |  |  |  |  |  |
| No. | Sequ.No. | Name | Quan. | Spec. | No. | Sequ.No. | Name | Quan. | Spec. |
| 1 | 0201 | Cabinet | 1 |  | 27 | 0227 | Six-angular nut | 2 | M8 |
| 2 | 0202 | Shelf for lubricant | 1 |  | 28 | 0228 | Rubber washer | 4 |  |
| 3 | 0203 | Cover of vertical arm base | 1 |  | 29 | 0229 | lever | 1 |  |
| 4 | 0204 | Lubricant box | 1 |  | 30 | 0230 | Round bolt | 4 | M5X10 |
| 5 | 0205 | Tire protecting pad | 1 |  | 31 | 0231 | Jointing shaft of bead breaker | 1 |  |
| 6 | 0206 | Round bolt | 4 | M6X16 | 32 | 0232 | Spring ring for shaft | 1 | D14 |
| 7 | 0207 | Block for air filter lubricator | 1 |  | 33 | 0233 | Flat washer ring | 4 | D8 |
| 8 | 0208 | Round bolt | 4 | M6X16 | 34 | 0234 | Inserting right angular pipe joint | 1 | D8 |
| 9 | 0209 | Jointing block for air filter lubricator | 1 |  | 35 | 0235 | O-ring | 2 | d 75x1.8 |
| 10 | 0210 | Air filter lubricator | 1 |  | 36 | 0236 | Guide cover | 1 | d 20 |
| 11 | 0211 | lower cover of cylinder | 1 |  | 37 | 0237 | O-ring | 1 | D24x2.4 |
| 12 | 0212 | Piston of cylinder | 1 |  | 38 | 0238 | Inner washer ring | 1 |  |
| 13 | 0213 | Upper cover of cylinder | 1 |  | 39 | 0239 | Out washer ring | 1 |  |
| 14 | 0214 | Threaded rod with double heads | 4 |  | 40 | 0240 | Inserting pipe joint | 1 | D8 |
| 15 | 0215 | Six-angular nut | 8 | M8 | 41 | 0241 | Nut | 1 | M12 |
| 16 | 0216 | Cylinder body | 1 |  | 42 | 0242 | Air supply joint | 1 |  |
| 17 | 0217 | Y-ring | 1 | D28 | 43 | 0243 | Air filter and lubricator | 1 |  |
| 18 | 0218 | Piston-rods | 1 |  | 44 | 0244 | Air pressure gauge | 1 |  |
| 19 | 0219 | Six-angular bolt | 1 | M12X120 | 45 | 0245 | Tee joint | 1 |  |
| 20 | 0220 | Six-angular bolt | 1 | M12X60 | 46 | 0246 | Pipe | 1 | Φ8 |
| 21 | 0221 | Spring washer ring | 2 | D12 | 47 | 0247 | Air filter and lubricator | 1 |  |
| 22 | 0222 | Six-angular nut | 2 | M12 | 48 | 0248 | Right angle terminal pipe joint | 1 |  |
| 23 | 0223 | Round bolt | 2 | M5X10 | 49 | 0249 | Pipe | 1 | Φ8 |
| 24 | 0224 | Left block | 1 |  | 50 | 0250 | Nut | 1 |  |
| 25 | 0225 | stick | 1 |  | 51 | 0251 | Pipe | 1 | Φ6 |
| 26 | 0226 | Round bolt | 2 | M5X40 | 52 | 0252 | Pipe | 1 | Φ6 |
|  |  |  |  |  | 53 | 0253 | Case cover | 1 |  |

| No. | Sequ.No. | Name | Quan. | Spec. | No. | Sequ.No. | Name | Quan. | Spec. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 0301 | Bottom board of foot pedal | 1 |  | 26 | 0326 | Round bolt | 2 | M6X10 |
| 2 | 0302 | Left foot pedal | 3 |  | 27 | 0327 | Flat washer ring | 2 | D6 |
| 3 | 0303 | Right foot pedal | 1 |  | 28 | 0328 | Spring of foot pedal | 3 |  |
| 4 | 0304 | Slide assembly | 1 |  | 29 | 0329 | Round bolt | 2 | M8X10 |
| 5 | 0305 | Slide rod | 2 |  | 30 | 0330 | Universal switch | 1 |  |
| 6 | 0306 | Protector of slide | 1 |  | 31 | 0331 | Spring | 1 |  |
| 7 | 0307 | bolt | 2 | M3X5 | 32 | 0332 | Round bolt | 1 | M4x10 |
| 8 | 0308 | Slide spring | 1 |  | 33 | 0333 | Pin | 2 | D2x20 |
| 9 | 0309 | Shaft of foot pedal | 1 |  | 34 | 0334 | Flat washer ring | 6 | D8 |
| 10 | 0310 | valve | 1 |  | 35 | 0335 | Flat washer ring | 16 | D6 |
| 11 | 0311 | Valve rod | 3 |  | 36 | 0336 | Valve | 1 |  |
| 12 | 0312 | Switch base | 1 |  | 37 | 0337 | Valve | 1 |  |
| 13 | 0313 | bolt | 2 | M5X20 | 38 | 0338 | Switch protector | 1 |  |
| 14 | 0314 | Jointing flake | 1 |  | 39 | 0339 | Bolt | 2 | 3x12 |
| 15 | 0315 | Spring base | 1 |  | 35 | 0335 | Flat washer ring | 16 | D6 |
| 16 | 0316 | Foot pedal joint spacer | 3 |  | 36 | 0336 | Valve | 1 |  |
| 17 | 0317 | Jointing rod of foot pedal | 1 |  | 37 | 0337 | Valve | 1 |  |
| 18 | 0318 | Six-angular bolt | 3 | M6X55 | 38 | 0338 | Switch protector | 1 |  |
| 19 | 0319 | Six-angular nut | 3 | M6 | 39 | 0339 | Bolt | 2 | 3x12 |
| 20 | 0320 | Round bolt | 14 | M6X15 | 40 | 0340 | Terminal pipe joint | 1 | D8 |
| 21 | 0321 | Round bolt | 3 | M4X25 | 41 | 0341 | Terminal pipe joint | 2 | D6 |
| 22 | 0322 | Six-angular nut | 3 | M4 | 42 | 0342 | silencer | 2 |  |
| 23 | 0323 | pad | 2 |  | 43 | 0343 | Pipe | 1 | Φ8 |
| 24 | 0324 | Six-angular nut | 4 | M8 | 44 | 0344 | Tee joint | 2 | D8 |
| 25 | 0325 | Six-angular nut | 14 | M6 | 45 | 0345 | Pipe | 1 | Φ8 |

| No. | Sequ.No. | Name | Quan. | Spec. | No. | Sequ.No. | Name | Quan. | Spec. |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 46 | 0346 | Pipe | 1 | Φ8 | 52 | 0352 | Pipe | 1 | Φ8 |  |
| 47 | 0347 | Right angle terminal pipe joint | 4 | D8 | 53 | 0353 | Joint | 1 | D8,D6 |  |
| 48 | 0348 | silencer | 4 |  | 54 | 0354 | Lines of motor | 1 |  |  |
| 49 | 0349 | Pipe | 1 | Φ8 | 55 | 0355 | Lines of power | 1 |  |  |
| 50 | 0350 | Pipe | 1 | Φ8 | 56 | 0156 | Pipe | 1 | Φ6 |  |
| 51 | 0351 | Pipe | 1 | Φ8 | 57 | 0249 | Pipe | 1 | Φ8 |  |
| No. | Sequ.No. | Name | Quan. | Spec. |
| 1 | 0401 | Arm of bead breaker | 1 |  |
| 2 | 0402 | Washer of bead breaker | 1 |  |
| 3 | 0403 | Axis of bead breaker | 1 |  |
| 4 | 0404 | Bead breaker | 1 |  |
| 5 | 0405 | Spanner | 1 |  |
| 6 | 0406 | Round bolt | 1 | M12X120 |
| 7 | 0407 | Six-angular nut | 1 | M12 |
| 8 | 0408 | Piston of big cylinder | 1 |  |
| 9 | 0409 | Piston-rods of big cylinder | 1 |  |
| 10 | 0410 | Cylinder body | 1 |  |
| 11 | 0411 | Cover of big cylinder | 1 |  |
| 12 | 0412 | Y-ring | 2 | 186 |
| 13 | 0413 | Y-ring | 1 | d 20xD30 |
| 14 | 0414 | Spring spacer | 1 | D30 |
| 15 | 0415 | Round bolt | 12 | M6X15 |
| 16 | 0416 | Flat washer ring | 12 | D6 |
| 17 | 0417 | Six-angular nut of flange for tightening | 12 | M6 |
| 18 | 0418 | Six-angular nut | 2 | M16 |
| 19 | 0419 | Right angular joint | 1 | D8 |
| 20 | 0420 | Large ring | 1 |  |
| 21 | 0421 | Round bolt | 1 | M8X10 |
| 22 | 0422 | Spring of arm of bead breaker | 1 |  |
| 23 | 0423 | pad | 2 |  |
| 24 | 0424 | Round bolt | 2 | M12X30 |
| 25 | 0425 | Flat washer ring | 1 |  |
| 26 | 0426 | Guide cover | 1 | d20 |
| 27 | 0427 | O-ring | 1 | d20x2.4 |
| 28 | 0428 | O-ring | 1 | D184x3.5 |
| 29 | 0429 | silencer | 1 |  |
| 30 | 0430 | Inner joint | 1 |  |
| 31 | 0431 | Quick exhausted valve | 1 |  |
| 32 | 0432 | Right angle terminal pipe joint | 1 | D8 |
| 33 | 0433 | Pressing button | 1 |  |
| 34 | 0434 | Protector of bead breaker | 1 |  |
| 35 | 0435 | Pressing button | 1 |  |
| 36 | 0436 | Adjusting washer | 1 |  |
| 37 | 0350 | Pipe | 1 | Φ8 |
| 38 | 0351 | Pipe | 1 | Φ8 |

| No. | Sequ.No. | Name | Quan. | Spec. |
| --- | --- | --- | --- | --- |
| 1 | 0501 | Lower cover of gear box | 1 |  |
| 2 | 0502 | Upper cover of gear box | 1 |  |
| 3 | 0503 | Gear box | 1 |  |
| 4 | 0504 | Bearing | 1 |  |
| 5 | 0505 | Axis of gear box | 1 |  |
| 6 | 0506 | Pin | 1 |  |
| 7 | 0507 | Bearing | 1 |  |
| 8 | 0508 | Rod gear box | 1 |  |
| 9 | 0509 | Bearing | 2 |  |
| 10 | 0510 | Seal-ring for shaft | 1 | D26 |
| 11 | 0511 | Round bolt | 5 | M8X25 |
| 12 | 0512 | Six-angular nut | 5 | M8 |
| 13 | 0513 | Big transfer wheel | 1 |  |
| 14 | 0514 | Pin | 1 |  |
| 15 | 0515 | Shelf for motor | 1 |  |
| 16 | 0516 | Alternator | 1 |  |
| 17 | 0517 | Small transfer wheel | 1 |  |
| 18 | 0518 | Six-angular bolt | 4 | M10X160 |
| 19 | 0519 | Flat washer ring | 10 | D10 |
| 20 | 0520 | Six-angular nut | 10 | M10 |
| 21 | 0521 | Six-angular bolt | 4 | M10X40 |
| 22 | 0522 | Flat washer ring | 8 | D10 |
| 23 | 0523 | Six-angular nut | 4 | M10 |
| 24 | 0524 | Transfer belt | 1 |  |
| 25 | 0525 | Six-angular round screw for tightening | 1 | M8X10 |
| 26 | 0526 | Spring spacer for shaft | 1 | D50 |
| 27 | 0527 | Valve | 1 |  |
| 28 | 0528 | Round bolt | 2 | M6X15 |
| 29 | 0529 | Pin | 1 | 12x8x50 |
| 30 | 0530 | Round bolt | 2 | M10x200 |
| 31 | 0531 | Seal-ring | 1 |  |

| No. | Sequ.No. | Name | Quan. | Spec. |
| --- | --- | --- | --- | --- |
| 1 | 0601 | turntable | 1 |  |
| 2 | 0602 | Clamp base | 4 |  |
| 3 | 0603 | Clamp | 4 |  |
| 4 | 0604 | Anti-friction flake | 4 |  |
| 5 | 0605 | S-plate | 1set |  |
| 6 | 0606 | Adjusting washer | 8 |  |
| 7 | 0607 | Joint shelf of cylinder | 2 |  |
| 8 | 0608 | connected board of slide | 2 |  |
| 9 | 0609 | Pin | 8 | Φ5x10 |
| 10 | 0610 | S-plate axis | 4 |  |
| 11 | 0611 | Cover of S-plate axis | 4 |  |
| 12 | 0612 | Ring of ring | 4 | D12 |
| 13 | 0613 | Six-angular bolt | 4 | M12X95 |
| 14 | 0614 | Flat washer ring | 4 | D8 |
| 15 | 0615 | Spring ring | 4 | D8 |
| 16 | 0616 | Round bolt | 4 | M8x25 |
| 17 | 0617 | Spring spacer ring for shaft | 1 | D75 |
| 18 | 0618 | Clamp protectors | 4 |  |
| 19 | 0619 | Blockage for turntable | 1 |  |
| 20 | 0620 | Six-angular nut | 1 | M16x30 |
| 21 | 0621 | Spring spacer ring | 4 | D12 |
| 22 | 0622 | Non-metal nut | 16 | M8 |
| 23 | 0623 | Back cover of cylinder | 2 |  |
| 24 | 0624 | Cylinder body | 2 |  |
| 25 | 0625 | Double heads bolt rod of cylinder | 8 |  |
| 26 | 0626 | Nut | 2 | M12 |
| 27 | 0627 | Out washer ring | 2 |  |
| 28 | 0628 | Rubber piston of cylinder | 2 |  |
| 29 | 0629 | Inner washer ring | 2 |  |
| 30 | 0630 | Piston rod | 2 |  |
| 31 | 0631 | O-ring | 4 | d 75x1.8 |
| 32 | 0632 | O-ring | 2 | D24x2.4 |
| 33 | 0633 | Guide cover | 2 | d 20 |
| 34 | 0634 | Y-ring | 2 | D28 |
| 35 | 0635 | Front cover of cylinder | 2 |  |
| 36 | 0636 | Flat washer ring | 8 | D8 |
| 37 | 0637 | Tee joint | 2 | D8 |
| 38 | 0638 | Pipe | 1 | Φ8 |
| 39 | 0639 | Screw pipe | 1 | Φ8 |
| 40 | 0640 | Right angular pipe joint | 2 | D8 |
| 41 | 0641 | Pipe | 2 | Φ8 |
| 42 | 0642 | Tee joint | 1 | D8 |
| 43 | 0643 | pipe | 1 | D8 |